## Slide 1: The State of the Planet
Sustainable Development Goals

## Slide 2: How do we make the most out of this learning opportunity?
Let’s build a community of learning
  Invitation to use AguaClara Gather as an open meeting spot
  Communicate more! (beware of the reluctance to communicate trap)
  Stop by and say hi!
Be skeptical, respectful, curious, and playful!

## Slide 3: Overview
Sustainable Development Goals
The value of safe water on tap
Intermittent Supplies (the spiral to failure or success)
The technology is well developed
A role for universities
Ctrl + click the pictures to go each section!

## Slide 4
2015 to 2030
Notes: On 1 January 2016, the 17 Sustainable Development Goals (SDGs) of the 2030 Agenda for Sustainable Development — adopted by world leaders in September 2015 at an historic UN Summit — officially came into force. Over the next fifteen years, with these new Goals that universally apply to all, countries will mobilize efforts to end all forms of poverty, fight inequalities and tackle climate change, while ensuring that no one is left behind.
http://www.un.org/sustainabledevelopment/development-agenda/

## Slide 5
“By 2030, achieve universal and equitable access to safe and affordable drinking water for all”
“Support and strengthen the participation of local communities in improving water and sanitation management” http://www.un.org/sustainabledevelopment/water-and-sanitation/

## Slide 6: WHO Fact sheet on water (2017): The good news
“In 2015, 71% of the global population (5.2 billion people) used a safely managed drinking-water service – located on premises, available when needed, and free from contamination.”
But let’s bring skepticism to this statement
This conclusion was made without collecting data on water quality in rural areas
This underestimates the billions who have unsafe water on tap!
(World Health Organization)
Notes: http://www.who.int/mediacentre/factsheets/fs391/en/
https://www.ircwash.org/blog/third-glass-three-quarters-full?utm_source=Amplify&utm_campaign=5c4000cc1e-Amplify_Aug_2017&utm_medium=email&utm_term=0_d60e6862b4-5c4000cc1e-48437621
Honduran government doesn’t even know how to contact the vast majority of the community water providers!

## Slide 7: UN Fact sheet on water (2017) The bad news
90% of the global population (6.8 billion people) used at least a basic service. A basic service is an improved drinking-water source within a round trip of 30 minutes to collect water.
884 million people lack even a basic drinking-water service, including 159 million people who are dependent on surface water
Globally, at least 2 billion people use a drinking water source contaminated with feces
Contaminated water can transmit diseases such diarrhea, cholera, dysentery, typhoid, and polio
Contaminated drinking water is estimated to cause 500,000 diarrheal deaths each year
Notes: http://www.who.int/mediacentre/factsheets/fs391/en/
Ridiculous number of significant digits. This is 1 billion and it might be 3 people…
This suggests that for a basic service it is okay if it contains feces.

## Slide 8: Honduras Stats as of 2015 (from WHO)
Population with sustainable access to an improved water source
  Urban – 97.4%
  Rural – 83.8%
Notes: http://apps.who.int/gho/data/node.main.46?lang=en

## Slide 9: Billions need Safe Water on Tap
Some three in ten people (2.3 billion) lack access to safe and readily available water at home (or maybe it is 5 in 10…)
Additional 1.2 billion from population growth gives 3.5 billion need water by 2030
  267 million people per year!
  800,000 L/s per year of new installed capacity
  Water for 18 New York Cities per year!
Notes: http://www.un.org/sustainabledevelopment/blog/2017/07/billions-around-the-world-lack-safe-water-proper-sanitation-facilities-reveals-un-rep
Assumes 3 mL/s
NYC is 1 BGD = 44000 L/s
18 NYC per year

## Slide 10: We forgot to include replacement of failing plants
Notes: La Esperanza, Honduras

## Slide 11: 4.4 billion need new water supply systems by 2030
50 year lifetime
8 years until 2030
16% of existing plants need to be replaced
Supposedly 5.6 billion have safe water on tap
0.9 billion need upgraded systems by 2030
The amount of infrastructure needed (and not yet built) to deliver safe water on tap to everyone on the planet is greater now than at any time in human history (Monroe’s opinion)

## Slide 12: Overview
Sustainable Development Goals
The value of safe water on tap
Intermittent Supplies (the spiral to failure or success)
The technology is well developed
A role for universities
Ctrl + click the pictures to go each section!

## Slide 13: Cost vs required personal effort: Current paradigm myth!
Per-capita cost
Personal (or household) effort required
Centralized water treatment and SWOT
Vended water
Ceramic filters
Boiling
POU chlorination
Solar Disinfection
Vended water is usually more expensive than SWOT
It is common for communities with poor water service to pay more for water than communities that have excellent service.
Ideally comes from a treatment plant
Where does the water come from?
Notes: Adapted from presentation by Amy Pickering at Cornell University in December 2018.
Cost of centralized water treatment is the treatment part! This forgets that in a city you need centralized water provision in any case.
Vended water means tanker trucks instead of a distribution pipe network!!!!! Are we really saying tanker truck water is cheaper than piped water????
If you don’t have a water supply system that you don’t have any water to boil.
Boiling doesn’t make water that is aesthetically pleasing.
This forgot to ask what the consumer wanted!
Check the math!

## Slide 14
Moroceli, Honduras
Distribution systems cost much more than treatment plants
Notes: Distribution systems cost much more than the treatment plant to build

## Slide 15: We are willing to pay more for better service
Cost of service ($/month)
Willingness to Pay ($/month)
How do we understand the failure of some systems?
Where is the “sweet spot” for sustainability?
Untreated river water at the tap
Traditional Mechanized plant
AguaClara plant
Service method
Break-even line
Minimum quality for public health
2
1
3
Providing a better service makes the whole system MORE sustainable
Notes: The cases of 1 (small towns less than 25,000) and 2 (towns larger than 25,000) in Honduras are the norm.
Sustainability is above the x=y line
Incremental cost for treatment is small! (both capital cost and operating costs)

## Slide 16: Conclusions: The value of safe water
There is a misperception that centralized water treatment systems are a bad idea. (Are roads, bridges, hospitals, and trains also a bad idea???)
The capital cost of delivering water on tap exceeds the capital cost of treating the water by perhaps a factor of 10
In order to be financially sustainable, drinking water suppliers must provide a service that is highly valued by the customers (a high quality product increases the revenue to maintain the system)

## Slide 17: Overview
Sustainable Development Goals
The value of safe water on tap
Intermittent Supplies (the spiral to failure or success)
The technology is well developed
A role for universities
Ctrl + click the pictures to go each section!

## Slide 18: Intermittent Supplies
It is estimated that over one-third of the urban water supplies in Africa, and in Latin America and the Caribbean, and more than half those in Asia, operate intermittently.
Why are supplies intermittent? _______________
  Crude form of rationing
  Lack of meters
  Leaking system – reduce amount of water lost
  Some sections of the city might never receive water otherwise
  Elevation challenges!
Rolling blackouts
Notes: http://www.who.int/docstore/water_sanitation_health/Globassessment/Global3.4.htm

## Slide 19: Leaks don’t cause contamination unless the flow is INTO the pipe
Necessary conditions:
  Saturated contaminated soil
  Leaky Pipe
  Pressure outside pipe must exceed pressure inside pipe
Potential Causes:
  Negative pressure transients
  Booster pumps
  Elevation changes
*Photo credits
Top: http://texas-slab-leak-repair.com/water_leak
Bottom: Emily Kumple
Notes: David Gold, Alicia Peters, Weier Chen,Lucia Garcia-Iturri Gallego, Distribution System Contamination Prevention
https://docs.google.com/presentation/d/1FbHpETKLk-6JZaqnlvxxkkQqu3iSUCvia9jvmYfr5kg/edit#slide=id.p21

## Slide 20: Booster pumps that pull water from the distribution system should be banned
Image credits: http://www.egr.msu.edu/~fultras-web/images/applications/gui/PressureWaveform.png
Emily Kumple
Pressure Transients
Boster Pumps
Notes: David Gold, Alicia Peters, Weier Chen,Lucia Garcia-Iturri Gallego, Distribution System Contamination Prevention
https://docs.google.com/presentation/d/1FbHpETKLk-6JZaqnlvxxkkQqu3iSUCvia9jvmYfr5kg/edit#slide=id.p16

## Slide 21: The Point of Use (POU) Treatment Preference and the spiral to failure
A Hypothesis – Given that
  centralized water supply systems always have leaks
  intermittency is common when water is in short supply
  contaminated water can flow into the supply pipes when they aren’t pressurized
  Centralized systems often fail to meet standards
Use Household level (Point of Use) and reduce funding to maintain the central water supply system
What happens next? Think about your home town.
Notes: Discuss and then vote

## Slide 22: Overview
Sustainable Development Goals
The value of safe water on tap
Intermittent Supplies (the spiral to failure or success)
The technology is well developed
A role for universities
Ctrl + click the pictures to go each section!

## Slide 23: Technology isn’t the problem
Former World Health Organization Director-General: Dr Gro Harlem Brundtland speech at Cornell University in 2005
Loosely paraphrasing…
We have the technology to solve the world’s problems – what is missing is education, institutional capacity, and political will
Reflect! This was before electric cars
Notes: This is the “engineers are irrelevant hypothesis”.

## Slide 24
AND
Policy, Education, Institutions
Technologies

## Slide 25: Policy, Education, Institutions or Engineering
You can sometimes compensate for poor engineering by providing more inputs
  Energy – fossil fuels
  Education
  Money
  Management
  Labor
You can sometimes reduce this burden on society by improving the technologies
These factors are multipliers!!!!
and

## Slide 26: These factors are multipliers!!!!
1x1x1x1x1x0=0
  Energy x Education x Money x Governance x Labor x Technology = ?
1x1x½x1x1x2=1
Notes: You can sometimes compensate for poor engineering by providing more inputs
  Energy – fossil fuels
  Education
  Money
  Management
  Labor
You can sometimes reduce this burden on society by improving the technologies
These factors are multipliers!!!!

## Slide 27: Package Plants

## Slide 28
Dominant Design Constraint?
Notes: What was the constraint used to create this design???? Constraints matter! The design you create will strongly reflect the constraints that you used to guide the design.

## Slide 29: Failure to design for energy efficiency

## Slide 30: Failure to design for the Operator

## Slide 31: Failure to design for the Operator

## Slide 32: Failure to design for the Operator

## Slide 33: Overview
Sustainable Development Goals
The value of safe water on tap
Intermittent Supplies (the spiral to failure or success)
The technology is well developed
A role for universities
Ctrl + click the pictures to go each section!

## Slide 34: A Role for Universities
Develop new knowledge
Test the designs in pilot scale field trials
Make that knowledge available to the global community
Open source engineering!
Capacity building: training the trainers
Bring the power of automation to engineering design (Take Henry Ford’s idea out of the realm of widgets and into the realm of knowledge)

## Slide 35: Open-Source University-based Research and Development
Design Studio
Sustainable Infrastructure
New Theories
Research Laboratory
Safe water on tap
Journey Inward
Journey Outward
Notes: From the research lab to new understanding of the physics to the design studio to the construction site to the tap
"research invent design empower"

## Slide 36: Low Carbon Footprint Technologies
Previous generations of engineers designed infrastructure that required cheap fossil fuel
It is long past time for a new paradigm
The original motivation for developing energy efficient technologies was the majority world, but many of these technologies will be the preferred option for wealthier communities too
Everyone likes cheaper, better, and more reliable

## Slide 37: Hypotheses: The Grand Experiment
Technology should be designed based on the conditions under which it will operate
For infrastructure it is more efficient to disseminate knowledge than hardware
We can achieve higher coverage using a model of technology dissemination in which we share knowledge openly

## Slide 38: Where are we going?
Control and measure flow
Flocculation
Sedimentation
Disinfection
Filtration
The Challenge!