## Slide 1: Growth of Bacteria in Water Distribution Systems
Consumption of dissolved oxygen
Increased heterotrophic plate counts or coliform counts
  This does not imply a health risk
Decreased hydraulic capacity of the pipes
Formation of taste/odor compounds
  Geosmin, mercaptans, amines, tryptophans, sulfates
Increased rates of pipe corrosion (for metal pipes)
I don’t have any evidence that this biological growth has a significant public health impact
extra
Notes: Rittmann, B. E. and P. M. Huck (1989). "Biological Treatment of Public Water Supplies." Critical Reviews in Environmental Control 19(2): 119-184.

## Slide 2: Pathogen Growth in Distribution Systems (CDC)
Biofilms are coatings of organic and inorganic materials in pipes that can harbor, protect, and allow the proliferation of several bacterial pathogens, including Legionella and Mycobacterium avium complex (MAC).
Mycobacterium avium complex, MAC, is an opportunistic bacterial pathogen, is resistant to water disinfection (much more so than Giardia cysts), and grows in pipe biofilms
We need more data here! Is this a real public health threat?
This is inconsistent with the purported (but apparently inconsequential) beneficial role of biofilms in SSF
extra
Notes: http://www.cdc.gov/ncidod/eid/vol7no3_supp/hunter.htm
Mark W. LeChevallier, director of research at the American Water Works Service Company, discussed health concerns regarding biofilms in the drinking water distribution system. Biofilms are coatings of organic and inorganic materials in pipes that can harbor, protect, and allow the proliferation of several bacterial pathogens, including Legionella and Mycobacterium avium complex (MAC). Factors that affect bacterial growth on biofilms include water temperature, type of disinfectant and residual concentration, assimilable organic carbon level, biodegradable organic carbon level, degree of pipe corrosion, and treatment/distribution system characteristics. Chloramine is considerably more effective than chlorine for controlling Legionella in biofilms, presumably because chloramine is more stable and thus less reactive than chlorine, allowing it to penetrate the biofilm more deeply.
An important factor in distribution system contamination and bacterial growth on biofilms is transient water pressure fluctuations that create pressure waves that pass through pipes in the distibution system. During the negative portion of the pressure wave, a substantial amount of contaminated water (>1 gal per minute) from the outside can be pulled into pipes through a small leak. This problem is aggravated when sewer lines are placed close to water pipes. Dr. LeChevallier stated that a number of waterborne disease outbreaks have been linked to distribution system deficiencies. Among the agents of nosocomial waterborne disease is MAC. This opportunistic bacterial pathogen lives in water, is resistant to water disinfection (much more so than Giardia cysts), and grows in pipe biofilms.

## Slide 3: WHO on Regrowth
There is no evidence to implicate the occurrence of most microorganisms from biofilms (excepting, for example, Legionella, which can colonize water systems in buildings) with adverse health effects in the general population through drinking water, with the possible exception of severely immunocompromised people
Water temperatures and nutrient concentrations are not generally elevated enough within the distribution system to support the growth of E. coli (or enteric pathogenic bacteria) in biofilms.
Thus, the presence of E. coli should be considered as evidence of recent faecal contamination.
http://www.who.int/water_sanitation_health/dwq/en/gdwq3_4.pdf
Notes: http://www.who.int/water_sanitation_health/dwq/en/gdwq3_4.pdf

## Slide 4: WHO on Regrowth (2)
Viruses and the resting stages of parasites (cysts, oocysts, ova) are unable to multiply in water.
Relatively high amounts of biodegradable organic carbon, together with warm temperatures and low residual concentrations of chlorine, can permit growth of Legionella, V. cholerae, Naegleria fowleri, Acanthamoeba and nuisance organisms in some surface waters and during water distribution
http://www.who.int/water_sanitation_health/dwq/en/gdwq3_7.pdf
Where is the original research for these conclusions?
Notes: http://www.who.int/water_sanitation_health/dwq/en/gdwq3_7.pdf

## Slide 5: WHO Recommendations for Chlorine as Sole Treatment
Low turbidity (<30 NTU) and low chlorine demand
  Low turbidity probably means good quality groundwater (from a spring or from a well)
For effective use; pre-treat turbid water
  Pre-treat means using a particle removal technology first
  Surface water would generally not meet the NTU requirement
Chlorine requires process control (feedback based on residual chlorine concentration)
http://www.who.int/water_sanitation_health/dwq/0207tab20/en/
Notes: http://www.who.int/water_sanitation_health/dwq/0207tab20/en/

## Slide 6: Pathogen Poisson Process Probability
Suppose we have an average pathogen concentration of C in our drinking water
Suppose we drink volume V
What is the probability that we will ingest k pathogens?
Suppose V = 1 L, C = 2/L, what is probability of ingesting exactly 2 pathogens?
Notes: P 136 in Probability and Statistics for Engineering and the Sciences by Jay L. Devore (5th edition)

## Slide 7: Probability of k Pathogens
What is probability of k < (dose)?
  Let dose = 15
  Find cumulative probability for k=14
CV=15
45% chance of not getting sick!

## Slide 8: Find probability that k>0
CV=1
For CV = 1, Pk>0 = 0.63
For CV = 0.001, Pk>0 = 0.001
(converge for small CV)

## Slide 9: Effect of Pathogen Dose
What happens if the pathogen dose is 10 rather than 1?
Let’s assume that the concentration of this new pathogen is 10 times as great (CV=0.01)
What is the probability that you ingest 10 or more?
Pathogens with an infectious dose of 1 are potentially quite harmful even at very low concentrations!
Pathogens with an infectious dose>1 are not dangerous at low concentration!
For CV = 0.001, Pk>0 = 0.001
For CV = 0.01, Pk≥10 = 3x10-27

## Slide 10: Waterborne Disease Outbreaks in the US (1985)
G. lamblia was the most frequently identified pathogen for the seventh consecutive year, causing three (20%) of 15 waterborne outbreaks.
In each of the outbreaks, as in well-characterized waterborne outbreaks of giardiasis in the past, water chlorination had been maintained at adequate levels to make outbreaks of bacterial diseases unlikely, but the lack of an intact filtering system capable of filtering Giardia cysts, distribution system problems, and mechanical deficiencies allowed drinking water to become a vehicle of giardiasis.
Notes: http://www.cdc.gov/epo/mmwr/preview/mmwrhtml/00001765.htm

## Slide 11: Waterborne Disease Outbreaks (1993)
The majority of outbreaks (68%) during 1991-1992 were classified as AGI of unknown etiology
Water sampling showed the presence of coliforms and/or deficiencies in chlorination for 91% of these outbreaks
24 outbreaks (71%) were associated with contaminated untreated or inadequately treated groundwater
Two outbreaks were associated with treatment deficiencies in water systems using UV light for disinfection
Three protozoal outbreaks during 1991-1992 occurred in systems that were equipped with chlorine disinfection and met EPA coliform standards but were not equipped with filtration
If you believe chlorine is what prevents waterborne disease outbreaks, then you will look for deficiencies in chlorination
Notes: http://www.cdc.gov/epo/mmwr/preview/mmwrhtml/00025893.htm#00000446.htm
As in previous years (Figure_4), the majority of outbreaks (68%) during 1991-1992 were classified as AGI of unknown etiology. Although some outbreaks were rigorously investigated, for many of these, the search for a causative agent was limited or clinical specimens could not be or were not obtained in a timely manner. The likelihood of identifying an etiologic agent was equally low (approximately one-third) for surface water and groundwater sources. However, the agent was much more frequently identified for WBDOs in community systems (63%) than in noncommunity systems (17%), emphasizing the difficulty of investigating outbreaks affecting the transient populations that use noncommunity water. Although the clinical features of illness in more than half of the AGI outbreaks suggest a viral etiology, clinical diagnosis is not specific; the group of outbreaks of AGI probably includes viral, bacterial, and parasitic etiologies. Availability of rapid diagnostic tests for viruses and newly emerging pathogens can aid in identifying the causative agents of these outbreaks. Information about the pathogens responsible for WBDOs is important for evaluating the adequacy of current water treatment processes and regulations. Nevertheless, the water quality data from AGI outbreaks suggest that available water disinfection technology is not always in place or used reliably; for 91% of these outbreaks, water sampling showed the presence of coliforms and/or deficiencies in chlorination.
During 1991-1992, 24 outbreaks (71%) were associated with contaminated untreated or inadequately treated groundwater. Adequate, continuous disinfection of groundwater should reduce the occurrence of WBDOs, particularly in small systems in which intermittent contamination of wells and springs is difficult to detect or prevent. In addition, wells and springs must be protected from sources of contamination such as surface runoff, septic tank drainage, and sewage discharges.
Two outbreaks were associated with treatment deficiencies in water systems using UV light for disinfection. UV light can be an effective disinfectant if properly applied, operated, and maintained. It may be effective for disinfecting bacteria and viruses but not protozoa (20,21). Reduced efficacy of UV systems for colored or turbid water has been noted (22), and UV light is not approved by EPA for use in surface water systems or in groundwater systems under the influence of surface water. For many of the outbreaks associated with inadequately treated water, chlorination was not maintained consistently. Adequate, consistent levels of chlorine are particularly important for disinfection of relatively chlorine-resistant organisms such as Giardia (23). Unfortunately, Cryptosporidium is highly resistant to disinfection by chlorine. Ozone is more effective than chlorine against Cryptosporidium (24), but no residual disinfectant is provided with this treatment. Ozone may not be suitable for small systems because of expense and the technical expertise required, and it is used as a disinfectant by less than 1% of the drinking water systems that serve populations of more than 10,000. Therefore, efforts to reduce the risk of waterborne giardiasis and cryptosporidiosis should focus on source protection and removal of cysts and oocysts by filtration.
The SWTR requires filtration of all but exceptionally well-protected surface water sources, including groundwater influenced by surface water. The SWTR was promulgated to reduce the risk of disease caused by waterborne protozoal parasites. Three protozoal outbreaks during 1991-1992 occurred in systems that were equipped with chlorine disinfection and met EPA coliform standards but were not equipped with filtration. EPA is considering an Information Collection Rule (ICR) that would require larger water utilities to monitor for Cryptosporidium, Giardia, and perhaps other pathogens in source water and, under certain conditions, in treated water for 18 months. Under the ICR, careful laboratory analysis and quality control would be needed, and the currently available laboratory methods do not assess infectivity of cysts or oocysts. Epidemiologic studies in conjunction with information on the occurrence of cysts and oocysts in source water will be helpful in assessing waterborne disease risks, determining the need for an enhanced Surface Water Treatment Rule, and determining whether specific monitoring for protozoal pathogens is necessary to supplement the total coliform MCL. The water quality data collected for WBDOs in the years 1991-1992 indicated that coliforms were detected for 88% of the outbreaks with bacterial, viral, or unknown etiologies but only 33% of the protozoal outbreaks. These data suggest that the use of coliforms as indicators of water contamination is generally sound but may not be adequate to detect contamination by protozoa.
Four of the six surface water systems associated with WBDOs were equipped with filtration. In three of these outbreaks, raw water quality had deteriorated because of sewage effluents that were not appropriately diluted as a result of low stream flows during dry weather. During the outbreaks associated with these systems, filtration deficiencies were noted, with elevated turbidity in finished water. Decreased filtration efficiency combined with deterioration in raw water quality also contributed to the WBDO in Milwaukee (1993). Although turbidity measurements indicated inefficient operation of the filtration process for the water systems associated with the 1993 Milwaukee outbreak and one Oregon outbreak (May 1992), none of the then-existing EPA water quality regulations were violated. Outbreaks associated with filtered systems illustrate the importance of improved operation and monitoring of the filtration process and the necessity for multiple barriers; in addition to disinfection and filtration, protection of raw water quality is essential for preventing transmission of waterborne diseases.

## Slide 12: Waterborne Disease Outbreaks (1993)
Four of the six surface water systems associated with WBDOs were equipped with filtration.
  In three of these outbreaks, raw water quality had deteriorated because of sewage effluents that were not appropriately diluted as a result of low stream flows during dry weather.
  During the outbreaks associated with these systems, filtration deficiencies were noted, with elevated turbidity in finished water.
Decreased filtration efficiency combined with deterioration in raw water quality also contributed to the WBDO in Milwaukee (1993).
It appears that chlorination was unable to provide an effective barrier when filtration failed
Notes: http://www.cdc.gov/epo/mmwr/preview/mmwrhtml/00025893.htm#00000446.htm

## Slide 13: A fatal waterborne disease epidemic in Walkerton, Ontario
An estimated 2,300 people became seriously ill and seven died from exposure to microbially contaminated drinking water in the town of Walkerton, Ontario, Canada in May 2000
The Walkerton operators were asked to provide a chlorine residual (majority to be free chlorine) of 0.5 mg/L after 15 min.
Evidence at the Inquiry revealed that chlorine dosage practice at Well #5 was insufficient to achieve a 0.5 mg/L residual even in the absence of any chlorine demand.
Although the evidence did not allow for an estimate of the chlorine demand at the time Well #5 was contaminated, it was reasonable to assume that the contamination causing this outbreak was accompanied by a chlorine demand sufficient to consume entirely, or almost entirely, the low chlorine dose thereby allowing inadequately disinfected water into the distribution system
Evidence that chlorination that doesn’t produce a residual doesn’t provide protection
Notes: http://www.iwaponline.com/wst/04703/0007/047030007.pdf

## Slide 14: Calicivirus - An Emerging Contaminant in Water
Annual estimates among adults in the U.S. reveal approximately 267 million episodes of diarrhea leading to 612,000 hospitalizations and 3,000 deaths
In the last 3 decades it has become increasingly clear that viral agents are responsible for much of this public health burden
Human caliciviruses (HuCVs) have been estimated to cause 95–96% of nonbacterial gastroenteritis outbreaks (Fankhauser et al., 1998; K.Y. Green et al., 2000).
These viruses are considered ubiquitous in nature and stable in the environment, thereby increasing their propensity to spread and cause disease
Notes: Huffman, D. E., K. L. Nelson, et al. (2003). "Calicivirus—An Emerging Contaminant in Water: State of the Art." ENVIRONMENTAL ENGINEERING SCIENCE 20(5): 503-515.

## Slide 15: Calicivirus
Four genera
  Lagovirus
  Vesivirus
  Norwalk-like viruses (Noroviruses or NLVs)
  Sapporo-like viruses (Sapoviruses or SLVs)
Single structural protein that makes up the viral capsid
27-40 nm in diameter
Cause disease in humans
Notes: Huffman, D. E., K. L. Nelson, et al. (2003). "Calicivirus—An Emerging Contaminant in Water: State of the Art." ENVIRONMENTAL ENGINEERING SCIENCE 20(5): 503-515.

## Slide 16: Norovirus: Infectious Dose
Human volunteer feeding studies have determined the number of viral particles needed to initiate infection is 10 to 100
The infectious dose may well be the result of mass transfer limitations in the gut
  i.e. the virus needs to be transported to the villi in the gastric mucosa and attach to initiate infection
Thus it is likely that 1 viral particle is sufficient to initiate infection
Huffman, D. E., K. L. Nelson, et al. (2003).
Weber-Shirk

## Slide 17: Norovirus: Clinical Illness and Diagnosis
The most common symptoms of NLV infections include mild to moderate diarrhea, abdominal cramps, and nausea (Adler and Zickl, 1969; Hedberg and Osterholm, 1993).
Other symptoms may include headache, malaise, chills, cramping, and abdominal pain. Stools typically do not contain blood or mucus.
The onset of illness is generally within 24 to 28 h of exposure with a relatively short duration of illness (12 to 60 h).
Adult infection with NLV can be distinguished from bacterial pathogens such as Salmonella and Shigella due to its characteristic projectile vomiting (Adler and Zickl, 1969; Caul, 1996)
Notes: Huffman, D. E., K. L. Nelson, et al. (2003). "Calicivirus—An Emerging Contaminant in Water: State of the Art." ENVIRONMENTAL ENGINEERING SCIENCE 20(5): 503-515.

## Slide 18: Norovirus: Inactivation
A 1-log reduction in the RTPCR signal of Norwalk virus was observed after treatment with 2 mg/L monochloramine at pH 8 for 3 h
Norwalk virus appears to be fairly resistant to free chlorine and monochloramine
Notes: Huffman, D. E., K. L. Nelson, et al. (2003). "Calicivirus—An Emerging Contaminant in Water: State of the Art." ENVIRONMENTAL ENGINEERING SCIENCE 20(5): 503-515.

## Slide 19: Chlorine Disinfection Mechanisms*
Oxidation of membrane-bound enzymes for transport and oxidative phosphorylation
Oxidation of cytoplasmic enzymes
Oxidation of cytoplasmic amino acids to nitrites and aldehydes
Oxidation of nucleotide bases
Chlorine substitution onto amino acids
DNA mutations
DNA lesions
*It is possible that none of these mechanisms have been documented
(more likely)
Notes: Rittmann, B. E. and P. M. Huck (1989). "Biological Treatment of Public Water Supplies." Critical Reviews in Environmental Control 19(2): 119-184.

## Slide 20: Ammonia Reactions
Substitution reactions…
The combined chlorine maintains its oxidizing potential
Total chlorine is combined chlorine plus free chlorine
NH3(aq) + HOCl  NH2Cl+ H2O
NH2Cl + HOCl  NHCl2+ H2O
-3
-3
+1
+1
+1
Combined chlorine
extra
Notes: Rittmann, B. E. and P. M. Huck (1989). "Biological Treatment of Public Water Supplies." Critical Reviews in Environmental Control 19(2): 119-184.

## Slide 21: Breakpoint Chlorination
Removal of ammonia by chlorination
Oxidizing equivalents of chlorine are consumed
2NH3(aq) + 3HOCl  N2+ 3Cl- + 3H2O
-3
+1
0
-1
extra
Notes: Rittmann, B. E. and P. M. Huck (1989). "Biological Treatment of Public Water Supplies." Critical Reviews in Environmental Control 19(2): 119-184.

## Slide 22: Does Chlorine Completely oxidize organic matter?
Oxidation states
  Carbon in organic matter (-4)
  Carbon in carbon dioxide (+4)
  Chlorine in HOCl (+1)
  Chloride (-1)
Therefore should take 4 moles of chlorine (Cl2) per mole of organic carbon
23.6 g chlorine/g organic carbon
4HOCl + CH4  CO2 + 2H2O + 4Cl- + 4H+
NO!
extra