## Slide 1: Thought experiment time! Breakout rooms for 3 minutes, then vote!
We start with two surface water suspensions, one that looks clean enough to drink (5 NTU - about 5 mg/L) and one that looks like chocolate milk (500 NTU – about 500 mg/L). We set the coagulant dose to have similar coverage of the particles in both cases. After flocculation the concentration of primary particles that haven’t flocculated is 1 mg/L for the 5 NTU raw water.
What do you predict the concentration of primary particles will be for the 500 NTU raw water?
  0.1 mg/L – cleaner than 5 NTU suspension
  1 mg/L – same as 5 NTU suspension
  10 mg/L - somewhere in between
  100 mg/L - same fraction remaining as 5 NTU suspension
Notes: One goal of flocculation is to reduce the concentration of primary particles (the particles that were in the raw water) that haven’t attached to other primary particles.
The rate of collisions is super fast initially and then tapers off to a crawl as the particles are lower concentration and further apart. The final concentration is set by the slow process of aggregation when the particle concentration is low, so the initial concentration drops out of the equation as irrelevant. So we get almost the same final concentration independent of the initial concentration!

## Slide 2: Fluids deform continuously (velocity gradient - G) given a stress (t)
Velocity gradient
Dynamic viscosity
Kinematic viscosity

## Slide 3: Surface Water often has Natural Organic Matter (NOM)
Coagulant nanoparticles are sticky
Natural Organic Matter (NOM) is not sticky

## Slide 4: Pre-hydrolyzed coagulant precipitates as stable (and sticky) Al13 clusters (nano particles)
clay

## Slide 5: Coagulant precipitate nano particles are sticky!
Coagulant nano particles (sticky)
Dissolved organic matter (not sticky)
Clay (not sticky)
Notes: Take a sticky note and dip in sugar and then try to get it to stick to your bulletin board.

## Slide 6: Natural organic matter adsorbs to the coagulant nanoparticles and coats the sticky surfaces
Observations and a Geometric Explanation of Effects of Humic Acid on Flocculation Y Du, WH Pennock, ML Weber-Shirk, LW Lion Environmental Engineering Science 36 (5), 614-622 (2019)

## Slide 7: 4 Breakout Rooms: Choose a reporter and answer your breakout room number question
Why can’t two particles of different sizes collide in a shear flow?
Why does the floc formed from two smaller flocs have a greater mass (and volume) than the sum of the masses (volumes) of the two smaller flocs?
Why don’t any clay particles attach to each other (no flocs form!) when you add a small amount of coagulant to a raw water that also has dissolved organic matter in it?
What limits the size of flocs exiting the flocculator?
Notes: Have each team